## Slide 1: Exam Prep: Microsoft Technology Associate 98-365: Windows Server Administration Fundamentals

## Slide 2: Course Topics
Windows Server Administration Fundamentals
01 ¦ Server Overview
02 ¦ Managing Windows Server 2022
03 ¦ Managing Storage
04 ¦ Monitoring and Troubleshooting Servers
05 ¦ Essential Services
06 ¦ File and Print Services
07 ¦ Popular Network Services and Applications
Notes: 1 minute

## Slide 3: Server Overview
Module 1

## Slide 4: Objectives
Skills/Concepts | Objective Domain Description | Objective Domain Number
Installing Windows Server 2022 | Understand server installation options. | 1.3
Introducing Server Roles | Identify application servers. | 2.1
Comparing Physical Servers and Virtual Servers | Understand server virtualization. | 2.5
Selecting Server Hardware | Identify major server hardware components | 5.1
Identify Methods to Install Windows Servers | Understand updates. | 6.3
Notes: This should also be a review for the 70-642.

## Slide 5: Server
  A server is a computer that provides services, and a client is a computer that requests services.
  A network made up of servers and clients is known as a client/server network
  A server-based network is the best network for sharing resources and data, while providing centralized network security for those resources and data
  Networks using Windows Server are typically client/server networks
Notes: A computer is providing services and requesting services.
While computers with Windows Server 2003 and Windows Server 2008 are designed to provide services, they can also request services from other computers.

## Slide 6: Server Roles
  Windows Servers use ‘roles’ to define what services the server provides
  A server can have multiple roles installed
  When you are determining hardware and software needs, look at the role the computer needs to fill and the load the computer will be placed under
File Services
Web Services
Directory Services
Notes: Some of the more common server roles include:
  File services
  Print services
  Web services
  Remote access
  Application servers
  Email server
  Database server

## Slide 7: Selecting Server Hardware
  When choosing server hardware keep the following in mind:
    Performance - Servers are intended to provide network services to many users
    Availability - If the server fails or becomes unavailable, the issue will affect multiple people
    Cost – How to balance available budget with the goals of performance and availability
Performance
Cost
Availability

## Slide 8: Primary Subsystems
  Processor
  Memory
  Storage
  Network
  Failure in any of these subsystems can cause the entire system to fail
  They can also cause a bottleneck that can affect performance of the entire system

## Slide 9: Processor
  Processors are typically 64-bit, which can process faster than 32-bit processors
    32-bit processor – 4 Gigabytes of RAM
    64-bit processor – 1 Terabyte of RAM
  A processor can only work on a single process / thread at a time
  Time slicing enables multiple threads and applications to be running at the same time
  A multicore processor enables multiple threads / application instructions to be worked on at the same time
Notes: The clock speed of a processor is usually expressed in gigahertz (GHz).
Most of the processors sold today are multi-core processors, which are like having two or more processing cores packaged as one.
Today, the newer processors are 64-bit, which work faster than the older 32-bit processors.
With more data in memory, a 64-bit processor can work faster because it can access larger amounts of RAM instead of swapping data back and forth with the much slower disks

## Slide 10: Memory
  Random Access Memory (RAM) is the computer’s short-term or temporary memory
  It stores instructions and data that the processor accesses directly
  If you have more RAM, you can load more instructions and data from the disks
  Having sufficient RAM can be one of the main factors in your computer’s overall performance
Notes: Unfortunately, when power is cut to the RAM, like when you shut off your PC, the contents of the RAM disappear. This is the reason you use disks rather than RAM for long-term storage.

## Slide 11: Storage
  Traditionally, hard drives are half electronic/half mechanical devices that store magnetic fields on rotating platters
  Solid-state drives are electronic devices with no mechanical components
  Personal computers typically only have local storage consisting of internal hard drives
  Servers may also connect to external storage through a network-attached storage (NAS) or storage area network (SAN)

## Slide 12: Network
  A network connection enables a device to communicate with servers or the clients
  Most devices include one or more network interface cards or NICs
  Speeds of today’s network cards are 100 Mbit/second, while a typical speed for servers is 1 Gbit/second or faster

## Slide 13: Motherboard
  Motherboard is the main printed circuit board that brings these four subsystems together
  The processor plugs in or connects to the motherboard or system board enabling communication with the rest of the system
  The motherboard provides the electrical connections enabling components of the system to communicate
Notes: Although everything is made around the processor, the motherboard is considered the nervous system of the PC. Motherboard capabilities have been greatly expanded (most include sound and network connectivity), and you can further expand the capabilities of the system by installing expansion cards (sometimes referred to as daughter boards).

## Slide 14: BIOS
  Basic Input/Output System (BIOS) are the instructions that control most of the computer’s input/output functions
  BIOS functions include communicating with disks, RAM, and the monitor kept in the System Read Only Memory (ROM) chips
  By having instructions (software) written on the BIOS, the system already knows how to communicate with some basic components such as a keyboard and how to read some basic disks such as IDE drives
  The BIOS also looks for additional ROM chips that may be on the motherboard or on expansion cards that you add to the system
  Flashing the BIOS is the process of updating your system ROM BIOS
Notes: If you have not realized it by now, instructions written on the BIOS is software.
Unfortunately like any software, the BIOS may need to have a bug fixed or may need to be expanded to support a new type of hardware that did not exist when the BIOS was written.
Sometimes a newer BIOS version can lead to better system performance.
To overcome some problems, you should check with your system or motherboard manufacturer to see if they have a new version of the BIOS.
The process of updating your system ROM BIOS, is called flashing the BIOS.
Unfortunately, flashing the BIOS is a delicate process. If the process gets interrupted in the middle or you install the wrong version, your system may not become accessible and you may have to replace your motherboard to overcome the problem.

## Slide 15: Power Supply and Cases
  A case provides an enclosure that helps protect system components that are inside
  A case with the power supplies and additional fans are usually designed to provide a fair amount of airflow through the system to keep the system cool
  The power supply supplies electrical power to the mother board and components

## Slide 16: Ports
  Ports are plug sockets that enable you to connect peripheral deices to your computer
  Devices can include a printer, keyboard, mouse, external drive or another computer
  Types of ports:
    Ethernet
    Parallel
    PS/2
    Serial
    VGA
    USB
    SCSI
    HDMI
    Audio

## Slide 17: Ports

## Slide 18: Virtual Servers
  Virtual machines or virtual server technology enables multiple operating systems to run concurrently on a single machine
  Virtual servers allows for a separation of services so that changes on one virtual server do not affect the other virtual servers
  Virtualization offers a better way utilize hardware since most hardware is sitting idle most of the time

## Slide 19: Locating the Server
  After you select and purchase the server and its components, you also need to determine where to physically locate the server
  The server room is the work area of the Information Technology (IT) department that contains servers and most of the communication devices including switches and routers
  The room should be secure, with only a handful of people allowed to have access to it

## Slide 20: Software
  Software contains the instructions that the hardware follows, which make the computer do what it does.
  It provides us with an interface that we can use to configure and manage the computer
  Configuring a server:
    Select, install and configure the operating system
    Select, install and configure the services that the operating system provides
    Install and configure additional software on the server

## Slide 21: Windows Servers
  Windows NT (first released in 1993) is a family of operating systems produced by Microsoft
  Since then, Microsoft has built on the previous version and released:
    Windows 2000 Server
    Windows Server 2003
    Windows Server 2003 R2
    Windows Server 2008
    Windows Server 2008 R2
    Windows Server 2012
    Windows Server 2012 R2
    Windows server 2016
    Windows Server 2019
    Windows Server 2022

## Slide 22: Windows Server 2008 R2
  Windows Server 2008 R2 editions
    Windows Server 2008 R2 Foundation
    Windows Server 2008 R2 Standard
    Windows Server 2008 R2 Enterprise
    Windows Server 2008 R2 Datacenter
    Windows Web Server 2008 R2
    Windows Server 2008 R2 for Itanium-Based Systems
  Windows Server 2008 R2 is only available in 64-bit version

## Slide 23: Windows Server Roles
  A server provides services
  Windows Server 2008 R2 has organized the most common services into server roles
  A server role describes the function of the server
  Windows Server 2008 R2 server features are software programs that are not directly part of a role
  Server features augment the functionality of one or more roles to enhance the functionality of the server

## Slide 24: Full Installation and Server Core
  Starting with Windows Server 2008, you can install Windows in one of two modes (both of which are provided on the installation DVD) :
    Full Version
    Server Core
  The full installation has a fully functional GUI interface and supports installing all available server roles and other Microsoft third-party software
  Server Core installation provides a minimal environment with no Windows Explorer shell that only supports certain server roles
  Desktop experience
Notes: The full version is the normal version that you would expect from Windows with a fully functional GUI interface.

## Slide 25: Windows Server 2022 R2 System Requirements
Component | Requirement
Processor | Minimum: 1.4 GHz (x64 processor)
Memory | Minimum: 512 MB RAM
Disk Space Requirements | Minimum: 32 GB
Display | Super VGA (800 x 600) or higher resolution monitor
Other | DVD drive, keyboard and Microsoft mouse (or compatible pointing device), and Internet access

## Slide 26: Clean Installation
  A clean installation installs the operating system to a new directory
  Select a clean installation in the following cases:
    No operating system is installed on the computer
    The installed operating system does not support the installation or upgrade
    To configure a multi-boot configuration
    A clean installation is preferred
  Performing a clean install of an operating system can be the preferred method because all files are installed again
  The disadvantage is that the system and all of its software needs to be reinstalled, patched, and configured and data copied over, something that may take hours or even days

## Slide 27: Sysprep
  If a Windows installation is cloned, each target computer using the same image will have the same parameters, including the same computer name and security identifier (SID)
  For these computers to operate properly without conflict on a network, these parameters have to be unique
  To overcome these conflicts, you run the system preparation tool (Sysprep)
  Benefits of Sysprep
    Removes system-specific data from Windows
    Configures Windows to boot to Audit mode
    Configures Windows to boot to Windows Welcome
    Resets Windows Product Activation

## Slide 28: Unattended Installation
  An unattended installation enables you to automate the configuration and deployment of operating systems
  An answer file is used to perform an unattended installation of Windows
  An answer file is an XML file that stores the answers for a series of graphical user interface (GUI) dialog boxes
  You can use any text editor such as notepad to create and modify the answer file, Server Image Manager can also be used

## Slide 29: Server Image Manager

## Slide 30: Windows Deployment Services
  Windows Deployment Services (WDS) is a technology from Microsoft for network-based installation of Windows operating
  Windows Deployment Services is the updated and redesigned version of Remote Installation Services (RIS)
  The deployment of Windows can be fully automated and customized through the use of unattended installation scripting files
  Benefits
    Allows network-based installation of Windows operating systems
    Deploys Windows images to computers without operating systems
    Uses standard Windows Setup technologies including Windows PE, .wim files and image-based setup
    Create images using a reference computer using the Image Capture Wizard

## Slide 31: Windows Imaging Format (WIM) File
  Windows installation files can be distributed within a Windows Imaging Format (WIM) file
  WIM is the file-based imaging format that Windows Server uses for rapid installation on new computers
  WIM files store copies (known as images) of the operating systems
Notes: Windows Deployment Services uses the WIM files to install Windows.
If set up properly, you need to boot a computer with Windows PE 2.0 or 3.0 or perform a PXE boot. Windows Preinstallation Environment (Windows PE) 2.0 is a minimal Win32 operating system with limited services, built on the Windows kernel.
It is used to prepare a computer for Windows installation, to copy disk images from a network file server, and to initiate Windows Setup.

## Slide 32: Windows Licensing
  A software license is purchased from a software company like Microsoft that gives you permission to use a specific software package
  Most licenses from corporations such as Microsoft work more like a lease rather than a purchase of the actual software
  Licenses are typically purchased for a specific number of users

## Slide 33: Windows Activation
  Microsoft product activation, including Windows activation, is an anti-piracy technology designed to verify that software products are legitimately licensed
  Product activation is included in some technologies
  A product key is required to activate the product

## Slide 34: Windows Updates
  Windows update helps keep your computer safer and your software current by fetching the latest security and feature updates from Microsoft
  After installing Windows, run Windows Update to install and apply fixes, patches, service packs, and device drivers
  Automatic updating can be enabled to download and install important updates as they become available

## Slide 35: DEMO: Windows Update

## Slide 36
© 2012 Microsoft Corporation. All rights reserved. Microsoft, Windows, Windows Vista and other product names are or may be registered trademarks and/or trademarks in the U.S. and/or other countries.
The information herein is for informational purposes only and represents the current view of Microsoft Corporation as of the date of this presentation. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information provided after the date of this presentation. MICROSOFT MAKES NO WARRANTIES, EXPRESS, IMPLIED OR STATUTORY, AS TO THE INFORMATION IN THIS PRESENTATION.